## Slide 1: Implementation of Integrated Water Resources Management (IWRM) in INDONESIA
presented by:
Hari Suprayogi
Adolf Tommy M Sitompul
Directorate General of Water Resources
Ministry of Public Works
February 21, 2013
for D-8 Water Cooperation Meeting
21-22 February, 2013
Istanbul, Turkey

## Slide 2: Outline
General Information
Water Resources in Indonesia
Water Usage Condition
Water Demand
Water Storage Capacity
Water Quality Status
Water Demand in the year 2030
Strategy for Water Provision
Directorate General of Water Resources
Ministry of Public Works

## Slide 3: consists of about 17,508 islands of which 6,000 are inhabited, total land area of about 1.94 million km2

## Slide 4
Indonesia has varied rainfall distribution from 800–4,000 mm/year. The rainfall are mostly concentrated within 5 (five) months whereas the other 7 (seven) months faces dry season
Monthly Rainfall

## Slide 5: Other Information Related
The population is ± 237.6 million with growth rate of 1,49% (2010), 300 million in 2030,
Water Resources is regulated by Water Resources Law No.7/2004 and 6 Government Regulations, while Policy on National Water Resources is stated by Presidential Decree No. 33/2011,
Directorate General of Water Resources
Ministry of Public Works

## Slide 6: 2. Water Resources in Indonesia
Directorate General of Water Resources
Ministry of Public Works
KALIMANTAN
TP : 1008 PC : 98.8
SULAWESI
TP : 247 PC : 18.3
INDONESIA (TOTAL)
TP : 3221 PC : 16.8
PAPUA & MALUKU
TP : 981 PC : 251.5
SUMATERA
TP : 738 PC : 18.4
JAVA
TP : 187 PC : 1.6
BALI AND NUSA TENGGARA
TP : 60 PC : 5.5
TP = Total Potential (billion m3/yr)
PC = Per capita (1000 m3/cap/yr)

## Slide 7
Source:
WR Research Centre, 2012
Roadmap CC Water Sector, 2011
DMI (106 m3/yr)
34,100 (19.5%)
IRRIGATION (106 m3/yr)
141,000 (80.5 %)
Domestic & Municipal (106 m3/yr)
6,400 (3,7%)
UTILIZED (106 m3/yr)
175,100 (25.3%)
GAMBARAN UMUM POTENSI DAN KONDISI PEMANFAATAN AIR DI INDONESIA
UNUTILIZED (106 m3/yr)
516,200 (74.7%)
INDUSTRY (106 m3/yr)
27,700 (15,8%)
WATER AVAILABILITY (106 m3/yr) | 
POTENTIAL | ACTUAL
3,906,500 | 691,300
INDONESIA | 3,906,500
SUMATERA | 840,700
JAVA | 164,000
KALIMANTAN | 1,314,000
SULAWESI | 299,200
BALI + NUSA TENGGARA | 49,600
MALUKU | 176,700
PAPUA | 1,062,100
DISTRIBUTION
3. WATER USAGE CONDITION IN INDONESIA

## Slide 8
Chart: Hydropower Potential in Indonesia
Potential Hydro Capacity (2003) | 15587 | 4200 | 21581 | 10183 | 22371 | 624 | 430
Demand Capacity (2010-2019) | 13666 | 58617 | 3442 | 3140
Supply Capacity | 2940 | 21485 | 620 | 559
75 GW

## Slide 9: Ratio of Reservoir Storage
Ministry of Public Works
RESERVOIR STORAGE PERCAPITA BY REGION
Source:
World Bank, 2003; White, 2005; Grey and Sadoff, 2007; IMWI, 2006;
INDONESIA
52 m3/kapita (present)
920 m3/kapita in 2030.

## Slide 10: 4.Water Balance
No | Region | Availability (S) | Demand (B) | Balance (S-B)
 |  | x 10⁶ m³/yr | x 10⁶ m³/yr | x 10⁶ m³/yr
1 | Sumatera | 111,077.65 | 37,805.55 | 73,272.10
2 | Jawa – Bali | 31,636.50 | 100,917.77 | -69,281.27
3 | Kalimantan | 140,005.55 | 11,982.78 | 128,022.77
4 | Sulawesi | 34,787.55 | 21,493.34 | 13,294.21
5 | Nusa Tenggara | 7,759.70 | 2,054.04 | 5,705.66
6 | Maluku | 15,457.10 | 540.23 | 14,916.87
7 | Papua | 350,589.65 | 385.58 | 350,204.07
 | Indonesia | 691,313.70 | 175,179.29 | 516,134.41
Directorate General of Water Resources
Ministry of Public Works

## Slide 11: Water Availability vs. Water Demand
Directorate General of Water Resources
Ministry of Public Works

## Slide 12
Directorate General of Water Resources
Ministry of Public Works
SEDIMENTATION
URBANIZATION
DEFORESTATION
SEDIMENTATION IN RESERVOIR
+
EROSION & SEDIMENTATION

## Slide 13: Land Use Change (Citarum River Basin)
Directorate General of Water Resources
Ministry of Public Works
Year 2000
Year 2008
Chart: Land Use Change in Citarum RB
| Hutan | Permukiman
2000 | 71750 | 81686
2008 | 9968 | 172361

## Slide 14
Directorate General of Water Resources
Ministry of Public Works
Sedimentation at Sutami Reservoir
Brantas River Basin
Chart: Sutami Reservoir Capacity
| 1973 | 1977 | 1982 | 1987 | 1989 | 1992 | 1994 | 1997 | 2002 | 2004 | 2006 | 2009 | 2011
Available Dead Storage | 110 | 67.2 | 54.09 | 39.54 | 39.76 | 35.84 | 35.14 | 35.42 | 30.57 | 29.91 | 28 | 24.41 | 23.175
Gross Storage* | 343 | 261.68 | 221.29 | 192.41 | 192.39 | 189.97 | 186.27 | 183.24 | 176 | 176.03 | 174.7 | 165.19 | 158.918
Effective | 233 | 194.48 | 167.2 | 152.87 | 152.63 | 154.13 | 151.13 | 147.82 | 145.43 | 146.12 | 146.7 | 140.78 | 135.743
Total Storage** | 399.123 | 316.7415 | 275.29 | 245.3485 | 244.267 | 240.7855 | 236.024 | 231.9325 | 223.631 | 222.5995 | 220.208 | 210.699 | 204.426
* Gross Storage =Effec. + Dead Storage
**Total Storage = Gross + Flood Storage

## Slide 15: Number of Floods Occured in Indonesia
Ministry of Public Works

## Slide 16: Water Pollution
Directorate General of Water Resources
Ministry of Public Works
Fertilizer and pesticides
Waste from household
Waste from Livestock
Waste from industry
Impact:
Water quality deterioration

## Slide 17: WATER QUALITY STATUS OF RIVERS IN INDONESIA
Sources: Ministry of Environmentand DGWR,2009
Directorate General of Water Resources
Ministry of Public Works
No. | Quality Status | Quantity of Rivers | 
 |  | Upstream | Downstream
1. | Quality Standard Class II | 2 | -
2 | Mild Polluted | 20 | 14
3 | Moderate Polluted | 6 | 15
4 | Heavy Polluted | 4 | 3
Total |  | 32 | 

## Slide 18
Directorate General of Water Resources
Ministry of Public Works
WATER DEMAND (2010 – 2030)
Source: National Planning Agency, 2010
Notes: Untuk wilayah Jawa-Bali memiliki kebtuhan air untuk DMI paling tinggi, yakni pada tahun 2010 sekitar 23,1 Milyar m3/tahun, dan pada tahun 2030 kebutuhannya naik lebih dari 8 kali lipat yaitu hampir mencapai 190 Milyar m3/tahun.

## Slide 19: Water Transfer
Directorate General of Water Resources
Ministry of Public Works

## Slide 20
Directorate General of Water Resources
Ministry of Public Works
Law No. 7 / 2004 concerning Water Resources, which replaced Law No. 11 / 1974 concerning Irrigation.
In the new rule, the principle of water resources management are continuity, balancing, public advantage, unity, harmony, justice, autonomy, as well as transparency and accountability.
Water Resources Management shall mean the effort of planning, implementation, monitoring and evaluation in regard to the conservation of water resources, utilization, and the control of water destructive potential (Law 7/2004 article 1 point 7).
INDONESIA RULES IN WATER RESOURCES SECTOR

## Slide 21
Directorate General of Water Resources
Ministry of Public Works
E F F O R T S
PLAN
EXECUTE
MONITOR
EVALUATE
ACTIVITIES
CONSERVATION
1. Water sources protection and preservation
2. Water preservation
3. Water quality management & water pollution control
UTILIZATION
1. Administration
2. Supply
3. Usage
4. Development
5. Operation
CONTROL OF WATER DESTRUCTIVE POTENTIAL
1. Preventive
2. Handling
3. Recovery
Maintaining sustainable water resources supportability, capacity, and functionality
Sustainable water resources utilization, by prioritizing the fulfillment of public needs equally
Preventing, handling, and recovery of environment damages caused by water destructive potential
OBJECTIVES
Water Resources Management (Law No. 7 / 2004)

## Slide 22: BASIC REGULATION
LAW NO. 41 / 1999 : FORESTRY
LAW NO. 7 / 2004 : WATER RESOURCES
LAW NO. 26 / 2007 : SPATIAL PLANNING
LAW NO. 27 / 2007 : SMALL ISLAND AND COASTAL REGION
LAW NO. 32 / 2009 : ENVIRONMENTAL PROTECTION
GOVERNMENT REGULATION NO. 42 / 2008 : WATER RESOURCES MANAGEMENT
GOVERNMENT REGULATION NO. 43 / 2008 : GROUND WATER MANAGEMENT
PRESIDENTIAL DECREE NO. 12 / 2012 : RIVER BASIN
PRESIDENTIAL DECREE NO. 26 / 2011 : GROUND WATER BASIN
1

## Slide 23
Gov Reg. No. 42 /2008 on WRM
Final Draft Gov. Reg on Swamp
Gov Reg No. 38/2011 on River
Gov Reg No. 43/2011 on Ground Water
Gov Reg No. 20/2006 on Irrigation
Gov. Reg. No. 16/2005 on Drinking Water Supply System
Final Draft Gov. Reg on Water Use Right
Gov. Reg No. 37/2010 about Dam
Water Resources Law No. 7/2004
Presidential
Decree No.06/2009 on National Water Resources Council
Pres Reg No. 12/ 2008 on Water Resources Council
Presidential Decree 12/2012 on River Basin Territories
Pres. Decree No.26/2011 on Ground Water Basin
Minister Regulation No 4/PRT/M/2008 about Manual of Establishment Coordination Team for WRM and National Water Resources Council.
FAMILY TREE OF WATER RESOURCES LAW
Final Draft Gov. Reg on Lake

## Slide 24
Information :
C = Water Resources Conservation
U = Water Resources Utilization
DP = Control of Water Destructive Potential
PR = Public Role
WR-DIS = Water Resources Data and Information System
PR
U
DP
C
Process of Water Resources Management
Plan, Execute, Monitor, Evaluate
WR - DIS
Integrated Water Resources Management
Directorate General of Water Resources
Ministry of Public Works

## Slide 25: Integrated Water Resources Management
RBT (River Basin Territory) : a territory unit of WRM could be in one or more river basins and/or small islands.
The whole Indonesia : 131 river basin territories (RBTs) where 63 RBTs are central government responsibilities and the rest of 68 RBTs are local government responsibilities.
Central Government: responsible to manage inter-state, inter-provinces, and nationally strategic RBTs; Provincial Government: responsible with inter-districts RBTs ; District/Regency Government: responsible with RBTs in one district/regency.
The implementation of water management in RBTs : by river basin territory management units (river basin organizations/ RBO’s).
Have to established National Water Council, Provincial Water Councils and River Basin Territory Water Councils.
Directorate General of Water Resources
Ministry of Public Works

## Slide 26
Map of River Basin Territory (RBT)
Presidential Regulation No. 12 Year 2012
Indonesia has over 5590 rivers, these rivers are grouped into 131 river basins. The river basins are categorized into 5 strata’s of river basins, include:
No. | Criteria of River Basin | Sum
1 | State Trans | 5
2 | Provincial Trans boundary | 29
3 | National Strategic | 29
4 | Regency/City Trans boundary | 53
5 | Regency/City | 15

## Slide 27
Strategic plan, plan, implementation plan, feasibility study, program and activity
Water Resources Management Plan
Implemented based on
River Basin Territory
Implementation Plan
boundary
Directorate General of Water Resources
Ministry of Public Works
Feasibility Study
Program of annual activitis
Annual activities

## Slide 28
STATUS RB STRATEGIC PLAN & IMPLEMENTATION PLAN
Strategic Plan
Implementation Plan
Presidential Decree No. 33/2011 : 131 river basin teritory should have each Strategic Plan

## Slide 29
STATUS NATIONAL and PROVINCIAL WR COUNCIL
& RBT WR COUNCIL
Chart: 
| Belum Terbentuk | Sudah terbentuk dan dikukuhkan (Tatib, pembagian komisi) | Beroperasional & memiliki sekretariat
 | 30 | 33 | 29
RBT WR COUNCIL
Chart: 
 | 22 | 3 | 8
PROVINCIAL LEVEL WR COUNCIL
1 NATIONAL WATER RESOURCES COUNCIL (44 member : 22 Govt + 22 NGO)

## Slide 30: REAL TIME HYDROLOGICAL COLLECTION (TELEMETRY SYSTEM)

## Slide 31
RECIEVER
SERVER
TRANSMITTER
DATA ACQUISITION
MAIN OFFICE
CELLULAR PROVIDER
SITE
VIA SMS
Related Institution
Hydrological Data Telemetry System

## Slide 32: Input data for run-off analysis
Data Feed
Telemetry
Flood
Time
River discharge
accuration decreases
Lead Time
Detections
Run-off analysis
Warning
Response
Flood forecasting
Present condition
NWP
Satellite
Radar

## Slide 33: CHALLENGEs IN THE FUTURE in the context of Water Cooperation

## Slide 34
RATIO of RESERVOIR STORAGE PER CAPITA
At Present 
52 M3/Capita/Year
i.e achieving
100 M3/Capita/Year
Required Cost 
50 Billion USD
ALLOCATED BUDGET FOR DGWR = 1,8 Billion USD
IMPOSSIBLE IF ONLY FUNDED BY THE GOVERNMENT
PRIVATE SECTOR
should be involved

## Slide 35: THE POSSIBILITY OF PRIVATE SECTOR INVOLVEMENT
POTENCY IN THE WATER SECTOR :
CONSUMPTION OF WATER AS RAW MATERIAL IN THE PRODUCTION PROCESS,
FOR LEACHING PROCESS IN INDUSTRY,
SELLING THE MINERAL WATER FOR THE PUBLIC CONSUMPTION.
LEGAL ASPECT :
LAW NUMBER 7/2004 REGARDING WATER RESOURCES,
GOVT. REGULATION NO.38/2011 REGARDING RIVER.

## Slide 36
Potency in Water Sector
Conservation/Revitalization of Natural Lakes,
Existing Reservoir
to be operated by Private Sector,
LONG STORAGE,
The “former“river area,
Natural Lakes or Small Reservoir for REST AREA in the Toll Road/Highway,
Hydropower/Mini Hydro,
etc

## Slide 37
POTENCY OF COOPERATION IN THE FUTURE
ENGINEERING KNOWLEDGE
NEED OF EXPERTS IN WATER RESOURCES ENGINEERING
RESEARCH POTENCY

## Slide 38: Concluding Remarks
The development of water resources management in Indonesia has been promoted through the concepts of “Integrated Water Resources Management” (IWRM) based on economic efficiency, equity and environmental sustainability,
The main challenges for water resources manager and engineers is how to manage the available water for fulfilling the water demand as well as to conserve the environment,
Integrated Water Resources Management in Indonesia, in response to climate change phenomena, is implemented through holistic approach and strong institutional system involving all stakeholders.
Directorate General of Water Resources
Ministry of Public Works

## Slide 39
THANK YOU
TESEKKUR EDERIM

## Slide 40: Terima Kasih